PRODUCT NAME : BP 1200(1200 MHz 帶通濾波器)

PART NUMBER :

- ELECTRICAL CHARACTERISTICS:

This filter satisfies Table 1 at Temperature Range : -40 to +85℃

PASS BAND FREQUENCY	:fo= 950 ~ 1450 MHz

INPUT/OUTPUT IMPEDANCE :50Ω

Max. INPUT POWER    : 1 W

TABLE  1

| NO. | ITEM | SPECIFICATION |
| --- | --- | --- |
|  |  | Min | typ | Max |
| 1 | PASS BAND INSERTION LOSS |  | 0.5dB | 3.0dB |
| 2 | PASS BAND RETURN LOSS | 10 dB | 12 dB |  |
| 3 | STOP—BAND ATTENUATION | at 1600 MHz | 30 dB |  |  |
|  |  | at 2400MHz | 25 dB |  |  |
| 4 | MTBF | 5 years |

TYPICAL ELECTRICAL CHARACTERISTICS