1ch Mini Car DVR board

Description:

SD card video recorder board is a high-performance, high-definition digital video recorder; board is 60*45mm. It adapts MPEG-4 video compression, and single channel resolution  up to D1(704*576), 30fps, is a fully real-time, high-definition, low power consumption, easy-operated, super-smart professional DVR.

It supports power-up record, motion detect record, scheduled record, and manual record, SD card up to 32GB expandable, and directly playback by TV sets, monitor, and PC by SD card reader.

Features:

- MPEG-4 video compression

- D1(704*576) resolution

- MPEG-4/ASF video format, MP3 audio format

- Real-time stamp on videos, overwrite

- Manual/motion detect/scheduled/power-up record

- audio input, audio compression 8KHZ/ADPCM

- 5/15/30fps optional

- SDHC memory support, up to 32GB

- TV-out enables better resolution by TV set

- MPEG-4/ASF playback

- AV-IN, AV-OUT directly connect with camera, TV, monitor

- Support IR remote operation, built-in ADC for external keyboards

- Support manually snapshot, auto record by triggering port

- Built-in RS232 series port, enables external remote, keyboard for operation and software set-up

- 5-35V for wide power supply use

- Low power-consumption, 1W when standby, 2W when recording

- Electronic dog ensures normal working

- Board dimension: 60*45mm, net weight 100g, with position holes for different expandable use

Board application:

The board supports wide voltage input, suitable for all vehicles use; SD card for storage avoid vehicle shock; resolution D1/VGA/QVGA and frames 5/15/30fps optional for different requirements in different conditions.

Remote instruction:

▲ Screen icons instruction

△ Standby mode

- Recording mode

▲ Menu set up:

△ Image setting

△ Recording setting

△ Recording mode set up

Set the recording mode for system

△ Playback&video files

△ Recording mode set up

Times&GPS

There is timestamp only，NO GPS OPTION. Choose timestamp ON/OFF

THE Peripheral Interface:Look for Expand interface manual